## Slide 1
Downscaling the National Low-Carbon Strategy
for the building activities
PhD defence 24.06.2024
PhD candidate: Marin Pellan
Thesis director: Prof. Guillaume Habert (ETH Zürich)
Supervisors: Dr. Mathilde Louërat, Dr. Denise Almeida (CSTB)
Notes: Hello everyone, physically or online, today I will present parts of my PhD thesis entitled “Downscaling the National Low Carbon Strategy for Building Activities.” This research was conducted between the Chair of Sustainable Construction at ETH Zürich and the Scientific and Technical Center for Buildings in France, under the supervision of Prof. Guillaume Habert, Dr. Mathilde Louërat, and Dr. Denise Almeida.
First of all, I would like to thank all the members of the jury for reading the manuscript and attending this presentation. I would also like to extend my gratitude to Prof. Taras for being the chair of the jury

## Slide 2
Summary
Introduction & context
Research gaps, state of the art & research questions
Contribution of the thesis
  Emissions accounting and carbon budgets setting
  Exploratory decarbonisation pathways for residential buildings
  Prospective LCA for new construction
Conclusion & discussions
Notes: To guide you through the presentation:
First, I will introduce the context in which this research is grounded
Next, I will highlight the identified research gaps, how previous studies have addressed them and the proposed research questions of the thesis
Following that, I will focus on three key contributions of the thesis:
  The development of an emission accounting and carbon budget setting methodology.
  The creation of a framework for exploratory decarbonization pathways at the residential stock level.
  The establishment of a method to couple a building LCA database with prospective LCA tools.
Finally, I will close the presentation with some conclusions and outlooks for future studies.

## Slide 3
Climate objectives
Buildings GHG emissions
Climate and building policies
Introduction & context
Notes: In this first part, I will introduce the climate objectives at global and national level, and explain why buildings play a key role in climate change mitigation

## Slide 4
Introduction & context
Shrinking carbon budgets
Climate objectives
Buildings GHG emissions
Climate & building policies
Remaining carbon budgets
Low-Carbon National Strategy (SNBC)
Global Carbon Project (2023)
Ministry for Ecological Transition (2019)
Notes: In 2015, the Paris Agreement set long-term goals to limit global warming to well below 2°C, and to pursue efforts to limit it to 1.5°C by the end of the century. This urgency requires peaking emissions as soon as possible and transitioning to net-zero emissions.
A key implication of these goals is that our remaining carbon budgets are limited, demanding a sharp decline in emissions across all sectors.
At the national level, the Paris Agreement translates into the Low-Carbon National Strategy (SNBC). This strategy allocates sectoral carbon budgets among different macro-economic sectors, aiming for net-zero emissions by 2050.

## Slide 5
Introduction & context
Type and magnitude of building-related GHG
> 9% CO2
Operational GHG
Life-cycle GHG
+
=
Embodied GHG
> 37% CO2
Direct
Indirect
28% CO2
23% territorial GHG
9% footprint GHG
2.2tCO2/cap
*
**
* UNEP (2022), Global Status Report for Buildings and Construction (energy and process-related CO2, concrete, aluminium, steel, bricks and glass only)
*
*
Fossil fuels, biomass, F-Gases
Electricity, district heating
Construction
materials & equipment
** CITEPA & Ministère de la transition écologique (2019) (using direct emission-factors)
***
*** SDES (2023), L’empreinte carbone de la France de 1995 à 2022 (CO2, CH4 and N2O)
***
Climate objectives
Buildings GHG emissions
Climate & building policies
Notes: So why are we talking about buildings when we study climate change mitigation?
Buildings contribute to emissions in two main ways:
- First, there are operational emissions, which come from the use of buildings. These can be further divided into direct and indirect emissions.
- Second, there are embodied emissions, which are the emissions from the life-cycle of construction materials and equipment.
Globally, the life-cycle emissions of building activities account for around 40% of global CO2 emissions from energy and processes. This makes them a major concern for meeting our climate goals. In France, operational emissions make up 23% of territorial emissions in 2019. When considering life-cycle emissions, buildings are the second biggest contributor to the carbon footprint of French citizens, behind transport.

## Slide 6
Introduction & context
Building and climate legislation at EU and French levels
Energy Performance on Buildings Directive (EPBD)
Renovation Wave
Whole-Life Carbon limit values in some EU countries (Denmark, Netherlands)
Low-energy consumption residential building stock by 2050
In 2050, direct operational GHGE ~5MtCO2eq, fully decarbonise electricity grid
New building Environmental Regulation (RE2020)
Climate objectives
Buildings GHG emissions
Climate & building policies
Notes: To mitigate building life-cycle emissions, there are several pieces of legislation at different levels:
-At the EU level, we have the revised EPBD, which focuses mainly on reducing operational emissions. Additionally, the Renovation Wave initiative aims to foster the renovation of existing buildings. Some countries also have laws targeting life-cycle emissions of buildings, with specific limit values, although very few do.
-In France, the residential building stock must achieve low-energy consumption levels by 2050, with sharply reduced operational emissions. The new building environmental regulation is innovative as it addresses both operational and embodied emissions by setting declining and mandatory limit values to be met by 2031, although it only applies to new construction.

## Slide 7
Research gaps & state of the art
  Emissions accounting challenges for buildings
  Complexity of modelling buildings at scale
  Linking top-down and bottom-up visions
Research questions
Research gaps, state of the art & research questions
Notes: Now What are the identified research gaps related to these topics, how has research addressed them, and what have we learned from this to formulate our research questions?

## Slide 8
* IPCC guidelines (2006)
** EN-15978 (2012)
B6-B7
Transport
B6-B7
A1-A5
B1-B5
C1-C4
Research gaps, state of the art & research questions
Emissions accounting challenges for buildings
National
GHG inventory*
Buildings
GHG
Building
Direct
operational
emissions
Indirect
operational
emissions
Embodied
emissions
Energy
Industry
Waste
Agriculture
Land-use
Imported
Emissions
Building
LCA**
Lack of holistic view in
decarbonisation pathways
and sectoral carbon budgets
(Giesekam et al. 2018)
Research gaps
Research questions
Notes: One major gap is the disparity in systems for accounting for emissions. In national emission inventories reported to the United Nations, 'buildings' only refer to direct operational emissions, or B6-B7 phases in the building LCA system, which is used in building legislation.
This overlooks other emissions types, which are included in other sectors like industry or transport, as well as imported emissions which are absent from national inventories.
This lack of comprehensive accounting system affects decarbonisation pathways and sectoral carbon budgets, as they typically rely on the inventory format. As Giesekam pointed out, this leaves building stakeholders without a holistic view for effective mitigation strategies. It also creates a gap between climate policies, such as the SNBC, which rely on the inventory format, and sectoral policies, such as the building environmental regulation, which increasingly rely on life-cycle thinking.

## Slide 9
MICRO SCALE
(individual buildings)
MESO SCALE
(neighbourhood, city)
MACRO SCALE
(country, continent)
Research gaps, state of the art & research questions
Complexity of modelling buildings at scale
Research gaps
Research questions
Data granularity
Modelling challenges and complexity,
Policy relevance
Uncertainties
SPACE
TIME
Life-cycle assessment
Emissions accounting
Input-Output Analysis
Hybrid life-cycle assessment
Prospective studies
Building stock modelling
Notes: Now, let's explore how we model building life-cycle emissions and the methods we use.
This can be done at various levels, from micro to macro scale. For climate objectives, macro scale results are important. However, modeling at this scale presents complex challenges, such as data scarcity and methodological issues, including determining which buildings to model for relevant analysis.
Furthermore, adding a time dimension for future projections of building emissions increases uncertainties.
To address these challenges, several methods were studied in this thesis, shown in yellow, and extensively described in the manuscript. Some focus on a single scale, while others, like life-cycle assessment and building stock modeling, bridge different scales and are increasingly used at macro scale for climate policies. Recently, there has also been a rise in prospective studies at both international and national levels, which can help test different hypotheses about the future state of buildings and related sectors like the energy and industry sectors.

## Slide 10
Research gaps, state of the art & research questions
Linking top-down and bottom-up visions
Bottom-up benchmarks
Decarbonisation pathways
Carbon budgets
World
Country
Economic
sectors
Building(s)
2020
2035
2050
Top-down
Bottom-up
Priore et al. 2023 (Switzerland)
Horup et al. 2023 (Denmark)
Li et al. 2023
(UK, renovation)
Röck et al. 2023 (EU)
Mouton et al. 2024 (Belgium)
Zhang et al. 2024
Alaux et al. 2023
Building stock database
Building LCA database
Cross-sectoral
activities
Research gaps
Research questions
Notes: To reach our climate objectives while understanding the current state and possible evolution of buildings, two types of modeling are often used: top-down and bottom-up.
The first one helps downscale high-level objectives to lower levels, like countries, economic sectors or even individual buildings. This often requires to use effort-sharing principles which are extensively described in the literature. What is often critical in terms of methodology is to downscale from country to cross-sectoral activities, mainly because of the accounting challenges presented earlier.
The second one provides detailed data on the current state of buildings and practical implications of decarbonization strategies. It also allows to study interactions between different sectors.
Recently, several European studies have used these modeling types (as shown in blue). In addition, data availability from building stock databases and building LCA databases has increased, improving the relevance and possibility of bottom-up analysis.
However, the link between these modeling types, especially for the entire building stock and the different stock-level activities (new construction, renovation, demolition), remains underexplored. The goal would be to answer the question of how to better align actions with climate goals, and use detailed bottom-up data to study the conditions under which we can meet them.

## Slide 11
Research gaps, state of the art & research questions
Research questions
Emissions accounting and carbon budgets setting
How to develop carbon budgets for the building activities
and model exploratory decarbonisation scenarios by 2050 using life cycle thinking ?
Research question 1 (RQ1) :
Research question 2 (RQ2) :
Research question 3 (RQ3) :
How to highlight the different scopes of emissions (energy carriers and supply-chain emissions) and expand/complement existing sectoral climate policies?
Exploratory
decarbonisation
pathways
How can we assess the alignment of future residential emissions with predefined carbon budgets?
How do different building typologies perform in terms of embodied emissions now and in the future decades, when considering the decarbonisation of supply sectors?
Prospective
LCA
Research gaps
Research questions
RESIDENTIAL BUILDINGS
NEW RESIDENTIAL BUILDINGS
BUILDING ACTIVITIES
Notes: This exploration of the research gaps lead us to the research questions that we have identified in this thesis. The main question of this thesis is: 'How to develop carbon budgets for the building activities and model exploratory decarbonization scenarios by 2050 using life cycle thinking?'
To answer this, three sub-questions were tackled:
Relative to emission accounting and carbon budget methodology: How can we highlight the different scopes of emissions and expand or complement existing sectoral climate policies? In this first part, we cover the entire building activities.
Concerning decarbonization pathways and residential dynamics: How can we assess the alignment of future residential emissions with predefined carbon budgets? In this second part, we focus on the residential building stock.
Lastly, for future embodied performance of individual buildings: How do different building typologies perform now and in the future decades, when considering the decarbonisation of supply sectors?“. In this last part, we specifically target new residential construction.

## Slide 12
01. Emissions accounting and carbon budgets setting (RQ1)
Emissions accounting results in 2019
Carbon budgets results by 2050
  Operational budget
  Embodied budgets
Notes: Now let’s dive into the methodology and let’s begin with outlining the carbon budgets set for the French building activities by 2050.

## Slide 13
Scope 3 (FR)
1. Emissions accounting and carbon budgets setting
Downscaled climate goals: life-cycle carbon budgets by 2050
2030
2050
5.7MtCO2eq
0.9MtCO2eq
2019
Direct & Indirect
Operational GHG
Embodied GHG
49MtCO2eq
14MtCO2eq
83MtCO2eq
21MtCO2eq
58MtCO2eq
Stated Policies (SP)
Announced Pledges (AP)
Net Zero (NZ)
58MtCO2eq
52MtCO2eq
44MtCO2eq
SP
AP
56MtCO2eq
22MtCO2eq
2.2MtCO2eq
* Results were integrated in the French building activities decarbonisation roadmap (2023)
NZ
2.4°C
1.7°C
1.5°C
2.4°C
1.7°C
1.5°C
40%
60%
RQ1
Notes: Because of time constraints, I will not go into the detail of the methodology here, which is fully described in the manuscript. It is just important to note that operational emissions are calculated based on the national energy balance and life-cycle emission factors, while embodied emissions are calculated using a multi-regional input-output database called Exiobase
I will now go directly to the results, which are the emissions and carbon budgets results for the different scopes of emissions. In 2019, operational emissions dominate with 65% of the total life-cycle emissions, while 60% of embodied emissions come from abroad. To translate these results into 2050 goals, operational emissions are projected using the SNBC buildings and energy pathways which assume a rapid and steep decrease. Embodied emissions are projected using three scenarios proposed by the International Energy Agency, which lead to different temperature outcomes by the end of the century, through the decarbonisation of the different sectors involved in the building activities supply chains.
In 2050, under the combined SNBC and Announced Pledges Scenario, which assumes all climate policies by countries are fulfilled, life-cycle emissions of French buildings should be below 30MtCO2eq. Under the Net Zero Scenario, emissions are projected to be under 10 MtCO2eq.
It should be noted that the SNBC does not transparently display the effort-sharing principle used for downscaling at the national level, and its sectoral pathways are based on multiple models that are not fully integrated. In the IEA scenarios, the pathways are based on techno-economic models that integrate the decarbonisation potential and costs of the different sectors.

## Slide 14
Methodology
  Framework
  Designing scenarios
Results
  GHG in 2050
  Pathways
  Cumulative GHG
02. Exploratory decarbonisation pathways for residential buildings (RQ2)
Notes: Now that we have our carbon budgets objectives for the building activities, how can we assess the alignment and compatibility of the residential dynamics and its associated emissions?

## Slide 15
2. Exploratory decarbonisation pathways for residential buildings
Modelling framework
How do the current
residential stock will evolve?
How many additional buildings
should we expect?
How will buildings be supplied in energy and materials?
Methodology
Results
Stock dynamics
Supply-side
Electricity
Gas, district network
Embodied performance
RQ2
Notes: So for that we have created a framework to study future possible emission levels starting from the current residential stock?
We can break this down into three sub-questions for which we have integrated and designed scenarios and methods.
The first one is : How many additional buildings will we have?
  For that we have calculated the yearly demand based on expected population growth, needs and demolition surfaces
The second one is: How will the existing building stock evolve through renovation and demolition?
  Here, we have relied on a building stock database and existing energy simulation, which included a potential state after renovation. We have also integrated differences renovation paces to analyze the effect of the distribution of the efforts over the next decades.
Finally the third one is: How will buildings be supplied in energy and materials?
  Here, we have first integrated different national scenarios for three energy carriers, namely electricity, gas and district network. And we have assumed different levels of embodied performance, in alignment with the environmental regulation.
The first two questions relate to the dynamics of the residential stock while the last one is more focused on the evolution of the supply sectors.

## Slide 16
2. Exploratory decarbonisation pathways for residential buildings
Designing scenarios
High
Construction
Medium
Construction
High
Demolition
Medium
Demolition
High renovation
Middle renovation
High renovation
Middle renovation
+ pace scenarios
Stock dynamics scenarios
Supply-side scenarios
Operational GHG
scenarios
Embodied GHG
scenarios
RE2020
Constant
Energy performance targeting
Fossil fuels targeting
Targeting
variants
G  A
High GHG  Low GHG
(150 000/yr)
(90 000/yr)
(22% of 2020 dwellings**,
250 000/yr*)
(67% of 2020 dwellings**,
750 000/yr*)
(180 000 /yr*)
(110 000/yr*)
* Average number of dwellings 2020-2050
** Total number of dwellings 2020-2050
Middle of the road
SNBC
RE2020++
Methodology
Results
RQ2
Business-
As-Usual
(BAU)
scenario
Ambitious
(AMB)
scenario
Notes: Because there are many parameters involved in each subquestion, we can potentially build hundreds of scenarios by combining them. As a result, we have designed two main families of scenarios:
A Business-as-Usual Scenario: which continues the current trends in terms of construction and demolition
An Ambitious Scenario: which tends to avoid the demolition of existing buildings and the construction of new building.
Different renovation dynamics can then be combined to each of these scenarios. As well, thanks to the use of the building stock database, we are able to test different targeting variants, namely if we focus on renovating only based on the energy performance label or if we target the type of energy carrier used.
Different supply-side scenarios can also be combined. In particular, we have tested variants where we keep the same emission factors for all energy carriers or if we integrate the different scenarios shown previously for electricity, gas and district network. We have also tested variants where the decreasing levels of embodied performance stop in 2031, as expected in the Environmental regulation, of if the decreasing trend continues up to 2050.
The results presented after will be the combination of the red parameters for the BAU scenarios and the green parameters for the ambitious scenarios.

## Slide 17
2. Exploratory decarbonisation pathways for residential buildings
2050 residential GHG in BAU and AMB
SNBC-Net Zero < AMB scenario < SNBC-Announced Pledges
Ambition ⬈  % embodied GHG ⬈ ⬈
(35% of life-cycle emissions in 2019 vs 50% in 2050 in AMB scenario)
% Indirect operational emissions ⬈ ⬈
(13% of life-cycle emissions in 2019 vs 26% in 2050 in AMB scenario)
Ambition ⬈  % Direct operational emissions ⬊ ⬊
(51% of life-cycle emissions in 2019 vs 24% in 2050 in AMB scenario)
SNBC-Announced Pledges
(entire building activities)
SNBC-Net Zero
(entire building activities)
2050 GHG
AMB scenario
BAU scenario
Methodology
Results
RQ2
MtCO2eq/yr
10
30
20
Notes: Looking at emissions in 2050, we see a significant gap between the scenarios. When compared to the 2050 budgets, we see that the ambitious scenario is almost aligned with the SNBC-Net Zero budget, although the budget is defined for the entire building activities, and not just the residential activities. Therefore, this scenario lies between the Net Zero and the Announced Pledges scenario. In contrast, the BAU scenario exceed the SNBC-Announced Pledges scenario, therefore not reaching the 2°C objective of the Paris Agreement.
Looking at the share of the different scopes of emissions, we see two interesting observations:
First, the more ambitious the scenario, the greater the share of embodied emissions, reaching half of life cycle emissions in 2050 in the ambitious scenario.
Second, in both scenarios, we see an increasing share of indirect operational emissions, which can be explained by the increasing electrification of usage, resulting for a quarter of life-cycle emissions in 2050. In contrast, the more ambitious the scenario, the lower the share of direct operational emissions.

## Slide 18
2. Exploratory decarbonisation pathways for residential buildings
Decarbonisation pathways in BAU vs AMB scenarios
BAU scenario
AMB scenario
Operational GHG
Embodied GHG
5
Ambitious scenarios require:
  Elimination of fossil fuels
  Deep decarbonisation of low-carbon energy carriers (SNBC)
  Deep decarbonisation of construction materials (e.g. 120-180 kgCO2eq/m2 for new construction in 2050)
  (RE2020++)
20
Fossil fuels
Oil
Oil
Methodology
Results
RQ2
10
20
30
40
50
10
20
30
40
50
60
60
10
20
15
5
MtCO2eq/yr
10
20
15
5
MtCO2eq/yr
MtCO2eq/yr
MtCO2eq/yr
Notes: But how the different scope of emissions dynamically evolve over the next 3 decades ? Here, we can analyze the operational emissions (above) and the embodied emissions (below) of the two contrasted scenarios.
1) For operational emissions, there is a significant difference in absolute values between the scenarios. In the ambitious scenario, there are no fossil fuels after 2040, and emissions plateau around 5 MtCO2eq in the last decade. The BAU scenario, however, reaches about 20 MtCO2eq by 2050, with a significant share of natural gas still in use, although oil products are phased out by 2045.
2) For embodied emissions, the contrast in absolute terms is less pronounced, even if the ambitious scenario still shows lower values, especially from 2040 onwards. The main difference between the scenarios here is the share of the different stock-level activities in total embodied emissions. In the BAU scenario, new construction consistently accounts for over half of emissions, whereas in the ambitious scenario, emissions from renovations dominate rapidly.
3) Overall, the lessons are that reaching ambitious carbon budgets requires :
The rapid elimination of fossil fuels, which is comparatively the better targeting option in terms of emissions reduction as developed in the manuscript.
The availability and deep decarbonisation of energy carriers that are already relatively low-carbon today such as electricity and district heating
The availability and deep decarbonisation of low-carbon construction materials that enable to reach very ambitious embodied carbon performance levels.

## Slide 19
03. Prospective LCA for new construction (RQ3)
Methodology
  Building LCA database and prospective LCA
Results
  GHG in 2020, 2030, 2040 and 2050 under IMAGE RCP1.9 scenario
Notes: The last requirement regarding embodied emissions will be the focus of the next section, where we will discuss in detail how we can model the achievement of carbon targets using real buildings from a building LCA database. Indeed, for now, we have only discussed embodied emissions per square meter using the Environmental regulation declining limit values, but we do not know which types of buildings can achieve the targeted performance.

## Slide 20
National
building LCA
DB
Typologies
exploration
Today
benchmark
Comparison with
target values
from AMB scenario
1
2
Decarbonisation
pathways
3
Future
benchmark
4
5
3. Prospective LCA for new construction
Assessing future upstream embodied performance
Methodology
Results
RQ3
Notes: To deal with that issue, we have developed a methodology focused on new construction using the Environmental Regulation database, which contains thousands of building LCAs, although it is currently dominated mostly by individual housing.
First, the methodology involves exploring this database to identify different typologies based on their material composition and geometric attributes using association rule mining and clustering. Due to the growing number of buildings in the database, this approach can provide a better representativeness of newly constructed buildings, can enable to incorporate a wide variety of typologies, and potentially offers more complete information thanks to a complete bill of materials compared to relying on only a few archetypes.
Then, we first compare the current embodied performance of the selected buildings, for the entire buildings and separately for structural work, second work and technical groups. Next, we model how decarbonizing the supply sectors would impact the future performance of buildings and compare these results to the target values identified in the previous chapter. These target values reflect the declining embodied performance outlined in the ambitious scenario presented earlier, which assumes that the declining trends of the Environmental Regulation from 2022 to 2031 will continue until 2050, reaching very low values compared to today’s benchmark.

## Slide 21
Decarbonisation
of buildings
and building stocks
Demand-side
Supply-side
Construction materials production
Energy carriers
Sufficiency
Material mix / Design options
influence
influence
Influence/interact
3. Prospective LCA for new construction
Decarbonisation levers: demand and supply-side
** Creutzig et al (2021)
“modify demand for goods and services”**
“changes in energy supply, production technologies […] that keep demand by end users invariants”**
*
* Sacchi et al (2022)
Methodology
Results
RQ3
Notes: In this work, we focus on modeling the supply-side decarbonization lever using the Premise prospective LCA package. The supply side typically involves changes in energy supply, energy efficiency, the share of different production technologies, or the introduction of new technologies, without modifying end-use demand. Premise facilitates this by allowing modifications to the ecoinvent life-cycle inventory database based on scenarios from Integrated Assessment Models, which have the advantage of covering the entire economy. This enables us to estimate the future impact of different activities available in ecoinvent under various scenarios, such as the emissions resulting from the production of 1kg of cement under the IMAGE Integrated Assessment Model and a 1.5°C scenario.
Since we rely on building LCAs that include Environmental Product Declarations (EPDs), we created a matching system between ecoinvent production activities and the different EPDs, specifically modifying their production phases, namely the A1-A3 phase.
What we do not model in our framework are the demand-side decarbonization levers, which involve modifying the demand for goods and services. When applied to buildings, this can refer to sufficiency measures or changes in design options that promote material efficiency strategies, for example. We have not integrated these, and that constitutes a limitation of our framework in fully understanding the decarbonization potential of buildings.

## Slide 22
3. Prospective LCA for new construction
Future upstream embodied performance, IMAGE RCP1.9 scenario
Concrete structure building
Timber structure building
2020
2030
2040
2050
Methodology
Results
RQ3
kgCO2eq/floor area
Notes: Here we display the results for two buildings that have been chosen based on the typology exploration phase: one with a concrete structure and the other with a timber structure.
We use the IMAGE RCP1.9 scenario, aiming for a 1.5°C temperature increase, which is very ambitious in terms of decarbonization, including in so-called hard-to-abate sectors like cement and steel. This is only a scenario, not a projection of what will happen, and it does not necessarily reflect the technical feasibility described in industrial roadmaps.
In terms of net emissions, represented by the black line, we observe a clear difference between the buildings, where the concrete building uses more emissive materials, especially for the structural work whereas the wood building uses fewer and benefits from carbon storage, accounted for as negative emissions, resulting in lower net emissions.
When comparing the results to the target values per decade from the ambitious scenario, the concrete building clearly underperforms, especially after 2030. In contrast, the wood building meets and even exceeds the target values, except for 2050.
These initial results provide an estimate of the decarbonization potential from supply-side sectors. They indicate that this potential alone is insufficient to meet the target values linked to the ambitious scenario, especially after 2030 and for the buildings that have high market share today.

## Slide 23
Conclusion
Discussions, future outlooks
Conclusion and future outlooks
Notes: This is now time to conclude and outline the key achievements and messages of the thesis, as well as underlining the main outlooks for future research.

## Slide 24
Conclusion & future outlooks
Conclusion and future outlooks
RQ1:
Emissions accounting and carbon budgets setting
RQ2:
Exploratory
decarbonisation
pathways
RQ3:
Prospective
LCA
Building activities ~160MtCO2eq, e.g. 25% of French GHG footprint in 2019
Carbon budgets < 29 MtCO2eq in 2050
A holistic perspective on the French building and construction footprint (SBE2022 Berlin)
Integrating consumption-based targets into sectoral carbon budgets […] (in review)
In order to respect the budgets, we need to decarbonize “everything, everywhere, all at once”’
  Stock dynamics should embrace high renovation rate and lower construction rate
  Fossil fuels eradication is key to efficient decarbonisation
  Deep decarbonisation of energy vectors and construction materials is necessary
From limit values to carbon budgets […] (published in Building and Environment)
Decarbonisation roadmap for the building activities […] (CISBAT 2023)
Supply-side decarbonisation provide an important level, but is insufficient alone
Current market shares are not aligned with carbon budgets
Assessing current and future embodied emissions of new buildings […] (in review)
Land-use change emissions
Regionalisation, more sufficiency levers
Availability of LCI, full sector coverage and extending to renovation
Notes: To answer the research questions, we developed three key blocks:
First, we created a methodology to represent the life-cycle emissions of buildings and define carbon budgets that complement existing climate policies. Applied to France, this methodology showed that building activities emitted 160 MtCO2eq in 2019, and that carbon budgets need to drop at least below 30 Mt. This approach can also be applied to other countries, in particular European ones with similar data availability. A part of this work has been presented at the SBE Conference in Berlin, while another more complete article is currently under review. In terms of outlook, future studies could focus on a bottom-up estimation of land-use change emissions which were not integrated in the thesis.
Second, we developed a framework to link these carbon budgets to the dynamics of the residential building stock and its associated emissions. We integrated existing scenarios and used a building stock database to create different targeting variants. The results indicate that aligning with ambitious carbon budgets requires a combination of higher renovation rates, lower construction rates, rapid elimination of fossil fuels, and deep decarbonization of the energy and industry sectors to supply low-energy carriers and construction materials. These results have been published in Building and Environment, while a more proof-of-concept approach involving a component-based model focused on renovation has been presented in the CISBAT Conference in Lausanne. Here, an important outlooks lies into the regionalisation of the dynamics and the inclusion of more sufficiency levers, alongside the lower square meter per capita already included in the ambitious scenario.
Finally, we investigated how different new building typologies can meet carbon targets at the building level, both now and in the future. Using a building LCA database and prospective LCA tools, we modeled the decarbonization of supply sectors. The results show that even in very ambitious scenarios, achieving the targets is challenging, especially for buildings with high market share today. This highlights the need to model additional measures, such as demand-side measure, and rapidly changing the current market shares to meet climate objectives. This last piece of work is currently under review. Future studies should tackle the problem of life-cycle inventory availability, full sector coverage in prospective LCA tools and the extension of the presented results to renovation packages.

## Slide 25
HUGE THANKS to all the people
who contributed to the work presented,
Welcome any QUESTIONS
Notes: Before concluding this presentation, I would like to thank all the people who helped me, inspired me, gave me feedback, with whom I was able to have discussions and without whom I would not be able to present this work today. A special thanks to Jérémy and all members of the committee. Thank you very much for listening and I now welcome any questions.

## Slide 26
TOP-DOWN
BOTTOM-UP
METHODOLOGICAL APPROACH
BOUNDARY
ALL BUILDING ACTIVITIES
RESIDENTIAL ACTIVITIES
NEW RESIDENTIAL
CONSTRUCTION
Proposed methodology
Input-Output Analysis
National emissions accounting
Scenario analysis
Life-Cycle Assessment
Building stock modelling
Scenario analysis
Life-Cycle Assessment
Building stock modelling
Scenario analysis
Focus of the presentation
State of the art of studied methods
Related studies and databases
Proposed methodology
Notes: We have chosen a methodology that works like an upside-down pyramid, both in terms of approach and boundary.
Indeed, we move from a top-down to a bottom-up analysis and we start by studying all building activities, then focus on residential activities, and finally on new residential construction.
For each step, we use some of the methods mentioned earlier. We begin with input-output analysis and national emission accounting, then use building stock modeling techniques and life-cycle assessment. In each step, we incorporate different scenarios that are integrated into the method in various ways as we will later in the presentation.

## Slide 27
Outlooks for future studies
Extending the scope of emissions accounting
  Land-use change emissions
  Carbon storage and sequestration
Complexifying stock dynamics
  Regionalisation of modelling for new construction demand, renovation and demolition potential
  Adding additional sufficiency levers
Continuing the linkage between prospective LCA tools and building LCA database
  Urgent need of life-cycle inventories for integration in building LCA database
  Similar exercises for renovation needs to be done
  Complete coverage of sectors in prospective LCA tools (e.g. heat production)
Further exploring the decarbonisation levers inter-dependencies
  Dependencies between decarbonisation levers (Avoid / Improve / Shift)
  Potential competition between technologies
Conclusion
Discussions & outlooks
Notes: Turning to future studies, the current blocks can be improved in several ways:
First, the current scope of emission accounting does not include land-use change emissions. These can be added using bottom-up estimation to provide more detailed location-specific data, compared to national inventories. Additionally, we have excluded the quantification of carbon storage and sequestration in buildings, which can also be integrated separately in future methodologies.
Second, the current modeling of stock dynamics was done at the national level. However, certain dynamics might be more relevant if studied at regional or city levels. For example, new construction demand could be differentiated between regions based on socio-economic parameters. Future studies should also integrate other sufficiency levers, such as lower vacancy rates or changes in building usage, alongside the lower square meters per capita already included in the ambitious scenario.
Third, we provided a proof of concept that combines a building LCA database with prospective LCA tools. The main obstacle for a full integration is the availability of life-cycle inventories. Future studies could address this by developing LCI archetypes for main construction materials. Additionally, what has been presented for new construction needs to be extended to renovations. Lastly, a complete coverage of sectors remains to be done in prospective LCA tool, with the heat sector being potentially very important for buildings.
Finally, a common outlook for all blocks is to study the interdependencies of decarbonization levers. This involves exploring how one type of decarbonization lever, such as 'avoid' solutions, can either hinder or accelerate other levers, like 'improve' or 'shift' solutions.

## Slide 28
Studied methods
Scale
Maturity
Standardisation
State of the art of studied methods
Related studies and databases
Proposed methodology
Input-Output Analysis
National emissions accounting
Hybrid LCA
Building Stock
Modelling
Life-Cycle Assessment (LCA)
Prospective studies
Notes: Are produced by different actors (statistical agencies, firms, NGOs, academia)
Have different boundaries/scope for example a rather large one with top-down vision, or a micro one with bottom-up
Have different existing standardisation or guidelines, and thus different levels of maturity
Finally the underlying data are more or less transparent

## Slide 29
Decarbonisation scenarios and roadmaps
Climate objectives
Carbon budgets for buildings
Decarbonisation scenarios
SECTORAL
MULTI-SECTORAL
NATIONAL
GLOBAL
Notes: A vast array of scenarios and modelling exercice is available with different levels of transparency on the data and modelling
Different levels of modelling transparency
Different levels of data availability
IEA more holistic cf equilibrium models

## Slide 30
Operational
emissions
National
energy
balance
Life-cycle
emissions
factors
x
Embodied
emissions
Multi-regional
input-output
database
+
F
Gas
National
input-output
statistics
+
2.1.1
2019
2050
Pathways
by
industries
Pathways
for
energy
carriers
GHGE accounting method at national level
2.1
Scenarios and decarbonisation pathways
2.2
2.1.2
National
decarbonation
pathways
International
decarbonation
pathways
01. Emissions accounting and carbon budgets setting
Emissions accounting and carbon setting methodology

## Slide 31
01. Emissions accounting and carbon budgets setting
Energy consumption and operational GHGE in 2019

## Slide 32
01. Emissions accounting and carbon budgets setting
Embodied GHGE in 2019

## Slide 33
01. Emissions accounting and carbon budgets setting
Embodied and Whole-Life Carbon budgets by 2050

## Slide 34
2. Exploratory decarbonisation pathways for residential buildings
EPC label matrix – Energy simulation results
Methodology
Results
RQ2
Notes: Looking at emissions in 2050, we see a significant gap between the scenarios. When compared to the 2050 budgets, we see that the ambitious scenario is almost aligned with the SNBC-Net Zero budget, although the budget is defined for the entire building activities, and not just the residential activities. Therefore, this scenario lies between the Net Zero and the Announced Pledges scenario. In contrast, the BAU scenario exceed the SNBC-Announced Pledges scenario, therefore not reaching the 2°C objective of the Paris Agreement.
Looking at the share of the different scopes of emissions, we see two interesting observations:
First, the more ambitious the scenario, the greater the share of embodied emissions.
Second, in both scenarios, we see an increasing share of indirect operational emissions
Because the remaining carbon budgets are about what is left to emit, cumulative emissions are also very important to look at. When we compare the scenarios from that metric, we also see a significant different, although it is less pronounced than for the 2050 emissions. So here, we see the relevance of starting to decarbonize the sooner possible to decrease the cumulative emissions.

## Slide 35
 | A | B | C | D | E | F | G
A |  |  |  |  |  |  | 
B |  |  |  |  |  |  | 
C |  |  |  |  |  |  | 
D |  |  |  |  |  |  | 
E |  |  |  |  |  |  | 
F |  |  |  |  |  |  | 
G |  |  |  |  |  |  | 
EPC label before renovation
EPC label after renovation
Demolition
Renovation
1
2
3
4
5
6
7
x
Modelling direction
2. Exploratory decarbonisation pathways for residential buildings
EPC label matrix – Renovation and demolition procedure

## Slide 36
(in surface)
For t in range (2020, 2050, 1)
m2/dwelling type
What is needed to satisfy population needs?
Based on demolition and (potential) additional needs, how much should we build?
How do we share this new surface between
individual/collective surface?
On average, what is the surface of one
individual/collective dwelling?
2. Exploratory decarbonisation pathways for residential buildings
Construction dynamics

## Slide 37
2. Exploratory decarbonisation pathways for residential buildings
Stock dynamics
Methodology
Results
RQ2
Notes: Looking at emissions in 2050, we see a significant gap between the scenarios. When compared to the 2050 budgets, we see that the ambitious scenario is almost aligned with the SNBC-Net Zero budget, although the budget is defined for the entire building activities, and not just the residential activities. Therefore, this scenario lies between the Net Zero and the Announced Pledges scenario. In contrast, the BAU scenario exceed the SNBC-Announced Pledges scenario, therefore not reaching the 2°C objective of the Paris Agreement.
Looking at the share of the different scopes of emissions, we see two interesting observations:
First, the more ambitious the scenario, the greater the share of embodied emissions.
Second, in both scenarios, we see an increasing share of indirect operational emissions
Because the remaining carbon budgets are about what is left to emit, cumulative emissions are also very important to look at. When we compare the scenarios from that metric, we also see a significant different, although it is less pronounced than for the 2050 emissions. So here, we see the relevance of starting to decarbonize the sooner possible to decrease the cumulative emissions.

## Slide 38
2. Exploratory decarbonisation pathways for residential buildings
Renovation paces
Methodology
Results
RQ2

## Slide 39
2. Exploratory decarbonisation pathways for residential buildings
2030, 2040 and 2050 GHG in BAU and AMB
Methodology
Results
RQ2
2050 GHG
2040 GHG
2030 GHG
AMB scenario
BAU scenario
AMB scenario
BAU scenario
AMB scenario
BAU scenario
Notes: Looking at emissions in 2050, we see a significant gap between the scenarios. When compared to the 2050 budgets, we see that the ambitious scenario is almost aligned with the SNBC-Net Zero budget, although the budget is defined for the entire building activities, and not just the residential activities. Therefore, this scenario lies between the Net Zero and the Announced Pledges scenario. In contrast, the BAU scenario exceed the SNBC-Announced Pledges scenario, therefore not reaching the 2°C objective of the Paris Agreement.
Looking at the share of the different scopes of emissions, we see two interesting observations:
First, the more ambitious the scenario, the greater the share of embodied emissions.
Second, in both scenarios, we see an increasing share of indirect operational emissions
Because the remaining carbon budgets are about what is left to emit, cumulative emissions are also very important to look at. When we compare the scenarios from that metric, we also see a significant different, although it is less pronounced than for the 2050 emissions. So here, we see the relevance of starting to decarbonize the sooner possible to decrease the cumulative emissions.

## Slide 40
2. Exploratory decarbonisation pathways for residential buildings
Average surface per EPC label and dwelling type
Methodology
Results
RQ2

## Slide 41
2. Exploratory decarbonisation pathways for residential buildings
Cumulative 2020-2050 GHG in BAU vs AMB scenarios
Carbon budgets
Methodology
Results
BAU scenario
AMB scenario
The sooner the reduction, the better
Non-linear budgets need to be developed
Notes: Because the remaining carbon budgets are about what is left to emit, cumulative emissions are also very important to look at. When we compare the scenarios from that metric, we also see a significant difference, although it is less pronounced than for the 2050 emissions. So here, we see the relevance of starting to decarbonize the sooner possible in order to avoid the important emissions of the first years.

## Slide 42
2. Exploratory decarbonisation pathways for residential buildings
Results – Targeting variants, example in BAU
Plateau from 2040 due to renovation of relatively poor energy efficiency housing (e.g., D-E) that already uses low-energy carriers
Energy performance label
Energy carriers
EPC targeting
Fossil fuels targeting
Carbon budgets
Methodology
Results
Notes: The operational emissions results presented before showed the fossil fuel targeting variant. Here, taking the case of the BAU scenario, we compare it with the energy performance targeting variant.
As we can see, in the last decade, there is a significant difference: the first targeting option shows a steep decrease, while the second shows a plateau.
This difference arises because, in the second targeting option, we target dwellings with medium to low energy performance that already use low-carbon energy vectors. Therefore, the emissions reduction is less advantageous compared to changing from fossil fuels to low-carbon energy vectors like electricity, biomass, or district heating.

## Slide 43
2. Exploratory decarbonisation pathways for residential buildings
Results – Cumulative GHG between scenarios
Carbon budgets
Methodology
Results

## Slide 44
3. Prospective LCA for new construction
Future upstream embodied performance, IMAGE RCP1.9 scenario
Methodology
Results
RQ3
Concrete structure building
Timber structure building

## Slide 45
3. Prospective LCA for new construction
Temporal profile
Methodology
Results
RQ3

## Slide 46
3. Prospective LCA for new construction
Clustering
Methodology
Results
RQ3
Variables:
Main structure
Roofs
Floors
Foundations
Confidence(X ⇒ Y ) = Support(X ∪ Y ) / Support(X)
Lift(X ⇒ Y ) = Confidence(X ⇒ Y ) / Support(Y )
Notes: This technique generates rules that depict the likelihood of associations between variables, facilitating the identification of recurring construction archetype patterns within the database. Key metrics in association rule mining include support, confidence, and lift.
-The support of an itemset X measures the frequency of variable association within the dataset
-Later, the confidence measures the probability of seeing the consequent given the antecedent
-Finally, the lift evaluates how much more frequently the antecedent and consequent co-occur than would be expected under statistical independence

## Slide 47
POPULATION
SUB-POPULATION
Stratification
Building stock DB
Clustering
1
2
3
Categorical var
Numerical var
MEDOID
4
Sampling and clustering procedure

## Slide 48
3. Prospective LCA for new construction
Clustering
Methodology
Results
RQ3
Notes: surface area, height, and specific areas for the building’s bay, wall and floor.